## Slide 1
INTERIM PROJECT REVIEW · JULY 2026
Real-Time Hydraulic Erosion Simulator
A Vulkan prototype that makes terrain change visibly, one water droplet at a time

## Slide 2
A static height map becomes a changing 3D landscape
01
Terrain is data
A 128 × 128 height grid comes from a PGM image or a procedural mountain.
02
Droplets are agents
Each droplet stores position, speed, water and carried sediment.
03
Capacity drives change
Under capacity: erode. Over capacity: deposit. Water evaporates over time.
04
Vulkan shows the result
The CPU updates terrain heights; the GPU redraws the mesh and visible droplets.
2

## Slide 3
Phases 1–5 now form a complete end-to-end prototype
The current build can load or generate terrain, animate water droplets and deform the 3D mesh in real time.
Phase 6 has started early
Live controls, pause/resume and 0.25×–8× simulation speed are already available.
✓
Phase 1 · Research and Vulkan pipeline
✓
Phase 2 · Height-map input and terrain mesh
✓
Phase 3 · Downhill droplet physics and debugging
✓
Phase 4 · Erosion, transport and deposition
✓
Phase 5 · Validation and mass-conservation tests
3

## Slide 4
A droplet behaves like a small truck carrying sediment
Capacity ≈ slope drop × speed × water × capacity factor
CAPACITY
Steep + fast + wet
The droplet can carry more material.
EROSION
Load < capacity
It removes soil and carries it downhill.
DEPOSITION
Load > capacity
It releases soil on gentler ground, then evaporates.
4

## Slide 5
Next: tune, benchmark and document the simulator
Jul 13–17 | Jul 20–24 | Jul 27–31 | Aug 3–14 | Aug 17–28
TODAY
Finish physics tuning + GUI
Presets + CPU profiling
CPU vs GPU benchmark
Paper: methods + results
Final review
Final outcome: a tuned simulator, measured performance and a complete report by 28 August 2026.
5